Ecotron
Assembly Manual

# Pin mapping
## SIM808 Module

SIM808	Arduino
RX	10
TX	8
DTR	11
RI	12
PWR	13
RST	Not used
VIO	Vcc
GND	Any GND
VBAT	Battery

Notes:
- RX/TX use SoftwareSerial library
- avoid using pin 13 as input
- SIM808 should not be powered via Seeeduino Stalker Vcc, which is regulated, for it may not be able to give enough power. Direct power supply from battery give better overall results.

## Temperature Sensor

Temperature sensor	Arduino
Vcc	Any Vcc
GND	Any GND
Signal	A0

## Ultrasonic Rangefinder Sensors

Can number	HC-SR04 module	Arduino
Far right (can 1)	Trigger	0
	Echo	1
Far left (can 5)	Trigger	4
	Echo	5
Middle left (can 4)	Trigger	6
	Echo	7
Close right (can 2)	Trigger	A1
	Echo	A2
Close left (can 3)	Trigger	3 (digital!)
	Echo	A3

Notes:
- Vcc and GND required for each sensor can be connected to any Vcc and GND
- positions refer to the actual container with 5 separate bins left and right as seen by device from within the container (not outside viewer!)
- from the outside, cans are conveniently ordered 1-5 from left to right

## Built-in connections

Sensor power switch – high on	9
RTC Hardware interrupt	2
RTC I2C SDA	A5
RTC I2C SCL	A4

Notes:
- Seeeduino Stalker 3.1 has a built-in FET that powers Vcc, controlled by pin 9 – use it to supply power to sensors
- RTC interrupt pin can be changed – don't

# Assembly

## Seeeduino Stalker

SD Card socket does not fit tight, fix it using some duct tape.

TODO: pic

## SIM808

All pins of SIM808 except RST are used, antennae are connected via uFL sockets.

TODO: pic

SIM card socket does not fit tight. To keep SIM in place, use a bit of duct tape.

TODO: pic

## HC-SR04 sensors

Note that wires are crossed. Labelling is handy.

TODO: pics

Sensor 3 is connected to one digital and one analog pin!

TODO: pic

## Sensor Shield

Note that battery and solar panel cannot be plugged in while sensor shield is in place – this is design flaw of Seeeduino Stalker.
However, plugging sensor cables is easier when shield is in place.

TODO: pic

## Power supply

Prepare the cable first: JST-PH goes to battery slot of Stalker, and another wire to VBAT of SIM808 module.

TODO: pic

Guess what, solar panel cables need to be soldered.

TODO: pic

And, plug them into Stalker, add sensor shield on top of it.

TODO: pic

# Programming

## Connecting programmer

Connect the thing to programmer – we use Foca by Itead.

TODO: pic

Plug USB cable into PC.

## Firmware changes

Each SIM cart has it's own PIN. In addition, depending on mobile operator, APN may need to be changed.
Look up PIN and APN in SIM808.ino, and set to your values, i.e.

// carrier data for GSM network
String PIN="8215";
String APN="mobileinternet.tele2.hr";

Server URL also needs to be changed, at least Station ID:

// server data
String SERVER="http://www.mikrotron.hr/ecotronserver/upload?stationId=gama";

## Testing

TODO

at+cmee=2

// runtime options
#define DEBUG true // run in debug mode
#define MANUAL true // manual control mode